| Layer | Misc. examples | TCP/IP suite | SS7 | AppleTalk suite | OSI suite | IPX suite | SNA | UMTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| # | Name |  |  |  |  |  |  |  |  |
| 7 | Application | NNTP, HL7, Modbus, SIP, SSI | DHCP, DNS, FTP, Gopher, HTTP, NFS, NTP, RTP, SMPP, SMTP, SNMP, Telnet | ISUP, INAP, MAP, TUP, TCAP | AFP | FTAM, X.400, X.500, DAP |  | APPC |  |
| 6 | Presentation | TDI, ASCII, EBCDIC, MIDI, MPEG | MIME, XDR, SSL, TLS (Not a separate layer) |  | AFP | ISO 8823, X.226 |  |  |  |
| 5 | Session | Named Pipes, NetBIOS, SAP, SDP | Sockets. Session establishment in TCP. SIP. (Not a separate layer with standardized API.) |  | ASP, ADSP, ZIP, PAP | ISO 8327, X.225 | NWLink | DLC? |  |
| 4 | Transport | NetBEUI, nanoTCP, nanoUDP | TCP, UDP, SCTP |  | ATP, NBP, AEP, RTMP | TP0, TP1, TP2, TP3, TP4 | SPX |  |  |
| 3 | Network | NetBEUI, Q.931 | IP, ICMP, IPsec, ARP, RIP, OSPF | MTP-3, SCCP | DDP | X.25 (PLP), CLNP | IPX |  | RRC (Radio Resource Control) |
| 2 | Data Link | 802.3 (Ethernet), 802.11a/b/g/n MAC/LLC, 802.1Q (VLAN), ATM, CDP, FDDI, Fibre Channel, Frame Relay, HDLC, PPP, Q.921, token ring | PPP, SLIP, PPTP, L2TP | MTP-2 | LocalTalk, TokenTalk, EtherTalk, AppleTalk Remote Access, PPP | X.25 (LAPB), Token Bus | IEEE 802.3 framing, Ethernet II framing | SDLC | RLC (Radio Link Control), MAC (Media Access Control), PDCP (Packet Data Convergence Protocol) and Broadcast/Multicast Control (BMC). |
| 1 | Physical | RS-232, V.35, V.34, I.430, I.431, T1, E1, 10BASE-T, 100BASE-TX, POTS, SONET, DSL, 802.11a/b/g/n PHY |  | MTP-1 | RS-232, RS-422, STP, PhoneNet | X.25 (X.21bis, EIA/TIA-232, EIA/TIA-449, EIA-530, G.703) |  | Twinax | UMTS L1 (UMTS Physical Layer) |